## Slide 1: The new Pbl_met
A library for the analysis and processing of micro-meteorological data
Mauri Favaron August 2018

## Slide 2: What is the pbl_met?
Fortran library
Open-source
License allows free use for commercial and non-commercial applications
Example uses
  1D meteorological processors (e.g. ST-Me, by Servizi Territorio srl)
  Ultrasonic anemometer data screening and preliminary processing
  SODAR and SODAR/RASS data validation and processing
  Narrow-beam weather radar (e.g. MRR2 by Metek GmbH) data processing
  Meteorological data validation

## Slide 3: Pbl_met Modules
pbl_base.f90 – Common conventions
pbl_time.f90 – Date-and-times; Basic astronomy (solar)
pbl_stat.f90 – Basic statistics; Time series
pbl_thermo.f90 – Thermodynamics; Psychrometry; Radiation models
pbl_evtrn.f90 – Evapotranspiration (Penman-Monteith ASCE ref equation)
pbl_wind.f90 – Anemology; Basic eddy covariance
pbl_simil.f90 – Monin-Obukhov similarity
pbl_depth.f90 – Mixing height; Dispersion indicators
pbl_met.f90 – Module collector; Single interface point

## Slide 4: The heritage of legacy pbl_met
The new pbl_met widely extends a pre-exixtent library, named PBL_MET (letter case is relevant)
Legacy PBL_MET was realized by prof. Roberto Sozzi and dr. Daniel Fraternali
Presented at Manno, 1994 (URL: http://www.harmo.org/conferences/Proceedings/complist.asp )
Specific focus: helping to craft 1D meteorological processors, for use in dispersion modeling
Intended users: expert atmospheric physicists
State: closed-source commercial library, then declassified (circa 2016) and placed to the open-source.

## Slide 5: Changes since legacy pbl_met
Focus expanded, from 1D met processors to general micro-meteorological data processing.
As a result, the code base enlarged significantly:
  Statistics!
  Eddy-covariance (wind, temperature, water (optional) and carbon dioxide (optional)).
  Support for sensors like ultrasonic anemometers (various data formats), SODAR/RASS and narrow-beam disdrometric radars.
Test suites now part of code base.
Example applications provided.
In general, extensive refactoring of legacy code.

## Slide 6: Test code
Quite a part of pbl_met is “test code”, aimed at harnessing procedure functionalities, and “proving” they are correct.
  For important modules, test code size equals or exceeds module size.
This is unlike the legacy PBL_MET, for which test code was not released.
Test code, collected under directory “/test”, also provides examples on using individual routines.
Test code also useful to see various modern Fortran constructs at work.
  Named optional parameters in argument list.
  Object-orientation.

## Slide 7: But: Why fortran?
To date, much scientific code is written using Python and R, so why indulging on Fortran?
Our main reasons are, small footprint and run-time efficiency.
Likely use cases:
  Real-time met processors on small scale embedded systems.
  Inclusion as component in meteorological and atmospheric pollutant dispersion models.
Besides, Fortran is still used and well known among the geophysicists community.

## Slide 8: Fortran specific advantages
In modern Fortran (i.e. Fortran 2003, 2008, 2015) extensive support is provided for current programming paradigms, e.g. object orientation and large-scale programming.
Modern Fortran natively supports parallelism, both fine-grained (e.g. SIMD) and coarse-grained (e.g. multi-core).
  Not directly used in pbl_met, but allowing easy inclusion in parallel code.
Very important (most, possibly): modern Fortran allows writing readable and understandable code.

## Slide 9: Code readability
The pbl_met places a very high value in readable and understandable code.
Our philosophy departs somewhat from open-source as traditionally intended in meteorology and atmospheric physics: we firmly believe there is no logical reason people, in front of a “public” project, should “sink or swim”.
Our purpose is not selecting tough contributors, but rather making life the least miserable possible to prospective users, who are not necessarily dedicated amateurs or professional programmers.
Because of this, pbl_met is “written for people” instead of “for the machine”.
And, high value placed for code whose meaning is transparent, even if this may decrease efficiency to some extent.